## Slide 1
Abellon CleanEnergy Limited comments on:
Draft Central Electricity Regulatory Commission (Terms and Conditions for Tariff determination from Renewable Energy Sources) Regulations, 2024

## Slide 2: Draft CERC RE Tariff Regulations, 2024
ANNEXURE A: For RDF-based Waste-to-Energy Projects
Sr. No. | Proposed Regulation | ACEL Comments
1. | Regulation 62 “CAPITAL COST” | CAPEX to provide for poor quality of waste (high moisture content and low calorific value) – requiring more CAPEX on pre-processing plants and FGCS. Consideration of real-time data from operational plants. Jamnagar WTE Plant: INR 19.33 Cr/MW (funding in 2019-21) Current pipeline projects: INR 22.33 Cr/MW (funding in 2020-22) MoHUA guidelines (Oct 2018) suggests pre-processing plant cost of INR 12 Cr/100 Tons ~ INR 120 Cr for a 14.9 MW. ACEL SUGGESTION: CAPEX to be determined in the range of INR 23 Cr / MW – INR 28 Cr / MW, including pre-processing infrastructure.
2. | Regulation 66 “FUEL COST” | Minimum boiler temperature of 850 °C required for combustion, to prevent emission of dioxin and furan. Needed for incineration of leftover waste during shut-down process. Poor quality of MSW makes it impossible for boiler to reach desired temperature during start-up procedure. CEA vide letter dated 06.03.2024 suggested that the Hon’ble CERC may allow mixing of supplementary fuel @ 5%. Biomass Tariff Order 2022 of Hon’ble GERC provides for supplementary fuel cost of INR 5,044 / MT with escalation @ 5.72% to the extent of 15% blending. Blending of supplementary fuel also supported by MNRE, GPCB and European Commission reports. ACEL SUGGESTION: 15% co-firing of supplementary fuel, cost @ INR 5,044 / MT @ 5.72% escalation.

## Slide 3: Draft CERC RE Tariff Regulations, 2024
For RDF-based Waste-to-Energy Projects
Sr. No. | Proposed Regulation | ACEL Comments
3. | Regulation 65 “O&M EXPENSE” | Determination cannot be based on simple comparative analysis of SERC findings. Should be based on real-time data from projects. Should consider component-wise cost (pre-processing plant, FGCS, ash & inert disposal) (detailed under Annexure – A5, Pg. 60-62). Higher O&M due to fluctuation in price caused by global unrest (Russia-Ukraine / Israel-Palestine wars), disruption in supply chain, nascent stage of technology and development. Expense of lime and activated carbon, specialized equipment, acquisition of skilled labour etc. to be accounted for in O&M expense. ACEL SUGGESTION: O&M not to be levelized, ought to be revisited and revised periodically.
4. | Regulation 64 “AUXILIARY CONSUMPTION” | To adequately provide for requirements of both Generating Plant and Pre-Processing Plant. Higher load on fans for side-wall cooling, flue gas recirculation and cylinder cooling to adequately incinerate heterogenous waste. Higher requirement due to FGCS, bag filters and boiler cleaning systems. ACEL’s real-time data suggests 18.87% requirement of aux. consumption. In line with MERC finding of 18.67% (Case No. 162 of 2019, order dated 22.03.2021). ACEL SUGGESTION: Auxiliary consumption of atleast 16%, if not 18.67%.

## Slide 4: Draft CERC RE Tariff Regulations, 2024
For RDF-based Waste-to-Energy Projects
Sr. No. | Proposed Regulation | ACEL Comments
5. | Regulation 14 “INTEREST ON LOAN” | Consideration of 200 basis points above average MCLR not accurate reflection of market trend. As per data from ACEL’s operational plant, fundings were provided with interest rate @ 11.95%. IREDA provided grants with interest @ 11.95%. ACEL SUGGESTION: Interest on term loan to be determined @ 11.95%.
6. | Regulation 15 “DEPRECIATION” | Trend of SERC findings suggest depreciation to be 7% for 1st 10 years, 2% for remaining useful life. To facilitate developers in repaying loans adequately and with ease. ACEL SUGGESTION: Depreciation @ 7% for first 10 years, 2% for period thereafter.
7. | Regulation 16 “RETURN ON EQUITY” | Developers import technology / equipment from abroad in bulk due to lack of adequate technology in India. Lucrative RoE important for attracting investment / fundings from venture capital / private equity / DFIs, who expect 25-30% returns. Calculation on MAT for first 20 years erroneous, since it is entire useful life of WTE plant. Should be MAT for 10 years, Corporate Tax for remaining period. ACEL SUGGESTIONS: MAT should only be considered for the first 10 years and applicable tax @ 27.82% to be considered for remaining period, RoE post-tax to be @ 18%.

## Slide 5: Draft CERC RE Tariff Regulations, 2024
For RDF-based Waste-to-Energy Projects
Sr. No. | Proposed Regulation | ACEL Comments
8. | Regulation 10 “TARIFF DESIGN” | Hybrid Tariff Model with two components: Levelized Tariff: Fixed Cost of project Non-Levelized Tariff: O&M, Fuel Cost fixed for first 3 years, to be reviewed at the upcoming control period.
ANNEXURE B: For Biomass Projects based on Rankine cycle technology
Sr. No. | Proposed Regulation | ACEL Comments
1. | Regulation 2 (c) “DEFINITION AND INTERPRETATION” | Definition of Biomass to include “organic fraction of MSW”. Recognized by BIS (Clause 3.8 of Indian Standard for Design, Construction, Installation and Operation of Biogas Plant) and MNRE (Guidelines for implementation of WTE Programme). National Policy on Biofuels, 2018 (clause 5.2) considers biomass as raw material for “advanced biofuel”. ACEL SUGGESTION: Biomass definition to include “organic fraction of MSW” as a part of Biomass.

## Slide 6: Draft CERC RE Tariff Regulations, 2024
For Biomass Projects based on Rankine cycle technology
Sr. No. | Proposed Regulation | ACEL Comments
2. | Regulation 31 “CAPITAL COST” | To adequately reflect high CAPEX requirement due to nascent stage of technology necessitating higher capital infusion. Historical failure of biomass plants and non-reflective tariff deters investment oppurtunities, hampers financial viability of projects. Availability of biomass fluctuates, owing to seasonal availability. Monsoon season increases moisture content, affecting boiler efficiency. Capital requirement increased for storage facility for surplus biomass. ACEL SUGGESTION: CAPEX of INR 90 lakhs – INR 1 Cr / MW to be added to the proposed CAPEX.
3. | Regulation 35 “O&M EXPENSE” | Higher O&M cost for individual and unique components (raw material, logistics, equipment, maintenance of grid-connected devices etc.) Lack of technological development, higher cost incurred for sourcing raw material from select sources. Overall price increased since no scope for scaling benefit. Costs due to transport of fuel to plant which are located in remote locations without proper access. Increased costs of handling, storage and transportation per unit since biomass has low energy density per unit of mass compared to fossil fuel. ACEL SUGGESTION: Normative O&M expenses for 1st year considered as INR 65 Lakhs / MW.

## Slide 7: THANK YOU